## Slide 1: Explainable ML-Learning‑Based Protection – Strategy
Goal today: show my plan (reading, models, data, lab tests, writing)
Notes: Today I want to present the overall strategy for my master's thesis on explainable learning-based protection.
The main goal is to investigate whether machine learning can improve protection performance in a challenging target fault regime where conventional relays are known to struggle.
I will first establish a conventional baseline relay and then compare several learning-based approaches against it.
The work is organized into five phases: literature review, framework development, data preparation, model evaluation, and validation. A key requirement is explainability, so I want to understand not only whether a model works, but also why it makes a trip decision.

## Slide 2: Overall workflow
Read & design
  Read Power System Relaying and ML‑for‑protection reviews…
  Fix target fault regime + conventional baseline relay
  Decide features and model families
Code framework
  Python project with modules for data, features, models, training/evaluation
Get data
  First: check for real / recorded relay data
  If not enough: create simulation dataset on a defined test system
Train, test, lab
  Train and compare models vs baseline using protection metrics
  Validate best model in lab / HIL setup (real‑time signals, latency)
Notes: Read & Design
The first step is a focused literature review on power system protection and machine-learning-based protection methods.
During this phase I will define the target fault regime, meaning the specific difficult operating condition that the thesis addresses.
I will also select a conventional baseline relay that represents current practice.
Finally, I will decide which protection features and model families will be investigated.
Code Framework
Before training models, I want a reusable Python framework.
The framework will contain separate modules for data handling, feature extraction, training, evaluation, and explainability.
This makes it easier to compare different architectures under identical conditions.
Data Acquisition
My first preference is to obtain real or recorded relay event data.
Real data is valuable because it reflects practical operating conditions and improves credibility.
If sufficient real data is not available, I will generate a simulation dataset using a defined test network.
The simulation dataset will include different fault locations, fault impedances, operating points, and DER penetration levels.
Train, Test, and Lab Validation
Once the dataset is available, I will train the selected models and compare them with the conventional baseline relay.
Evaluation will use protection-specific metrics such as dependability, security, selectivity, and operating time.
The best-performing model will then be validated in a laboratory or HIL environment.
This validation step is important to evaluate real-time behavior and inference latency.

## Slide 3: Model strategy
Core models (first):
  Tree‑based ensemble (Random Forest / Gradient Boosting)
    On engineered protection features; strong and interpretable baseline
  Shallow MLP (fully connected NN)
    On the same features; simple nonlinear model
Advanced models (after framework works):
  1D‑CNN on current/voltage windows – learns local transient patterns
  CNN‑LSTM / CNN‑GRU – CNN features + temporal evolution for evolving faults
  LSTM/GRU on time‑series or per‑cycle features – explicit temporal modelling
Notes: Core Models
I want to begin with models that are relatively simple, robust, and easy to interpret.
The first model family is a tree-based ensemble, such as Random Forest or Gradient Boosted Trees.
These models work well on engineered protection features and provide feature importance information for explainability.
The second model family is a shallow MLP using the same engineered features.
The MLP introduces nonlinear decision boundaries while remaining computationally manageable.
Advanced Models
After the framework is working, I will investigate more advanced architectures.
A 1D-CNN will process windows of current and voltage signals directly and learn local transient patterns.
CNN-LSTM or CNN-GRU architectures combine learned signal features with temporal modeling.
These architectures may be particularly useful for evolving faults or systems with dynamic inverter behavior.
I will also evaluate pure LSTM or GRU models to study the value of explicit temporal information.
Strategy
The goal is not simply to use the most complex model.
Instead, I want to understand the trade-off between performance, explainability, and computational requirements. Auto encouder

## Slide 4: Features & data plan
Features (from relays + papers):
  Per‑phase RMS currents/voltages, peaks
  Positive/negative/zero sequence components
  Apparent impedance / distance‑like quantities
  Frequency, RoCoF, dI/dt, dV/dt
  Harmonic / THD indicators (IBR and HIF behaviour)
Data:
  Try to use real / recorded relay events if available (for testing/generalization)
  Build simulation dataset if real data is limited (fault locations, impedances, operating points, DER levels)
  Later: use lab / HIL to feed real‑time signals to the best model
Notes: Features
The feature set is based on quantities commonly used in protection and reported in the literature.
RMS currents and voltages provide information about fault magnitude and operating conditions.
Positive-, negative-, and zero-sequence components capture fault asymmetry and unbalanced conditions.
Apparent impedance and distance-like quantities relate directly to traditional protection concepts.
Frequency, RoCoF, dI/dt, and dV/dt capture dynamic behavior and transient events.
Harmonic and THD indicators may be particularly useful in inverter-dominated systems and high-impedance fault scenarios.
Data Strategy
I will first investigate the availability of real or recorded relay event data.
Real data will be especially valuable for testing and assessing practical generalization.
If data is limited, I will create a simulation dataset covering a wide range of fault conditions.
The dataset will vary fault locations, fault impedances, operating conditions, and DER penetration levels.
Finally, laboratory or HIL testing will be used to expose the best model to real-time signals.

## Slide 5: Evaluation & explainability
Compare ML vs conventional baseline using:
  dependability, security, selectivity, operating time, sensitivity, misoperation rate, latency
  strict generalization: unseen fault locations/impedances
Explainability:
  Trees: feature importance, decision paths
  MLP/CNN/LSTM: SHAP / feature attributions and time‑series saliency, interpreted as physical quantities (e.g. negative sequence current, impedance entering zone)
Aim: show that the ML “relay” trips for physically meaningful reasons, not simulation artifacts
Notes: Comparison Against Baseline
All ML models will be compared against a properly tuned conventional baseline relay.
The baseline could be an overcurrent relay, distance relay, or another suitable protection function depending on the target fault regime.
The objective is to determine whether learning-based protection offers measurable improvements.
Protection Metrics
Dependability measures how reliably faults are detected and tripped.
Security measures how often unnecessary trips are avoided.
Selectivity evaluates whether the correct protection zone is identified.
Operating time measures the delay between fault occurrence and trip decision.
Sensitivity is particularly important for weak or high-impedance faults.
Misoperation rate summarizes overall incorrect decisions.
Inference latency evaluates computational feasibility for practical deployment.
Strict Generalization
A key requirement is strict generalization testing.
Some fault locations and fault impedances will be completely excluded from training.
This ensures that performance reflects genuine learning rather than memorization.
Explainability
For tree models, I will use feature importance and decision path analysis.
For neural-network models, I will use SHAP values, feature attribution methods, and time-series saliency techniques.
The explanations will always be interpreted using physical protection quantities.
The goal is to show that the model responds to meaningful electrical behavior rather than simulation-specific patterns.